How to install MPTK binary files

SUMMARY

Read this document to learn how to install the Matching Pursuit Tool Kit binary files on Unix platforms and MAC OS X.

# Getting started
## Required tools
- Optional (if Matlab interface is needed):
  - Matlab at least version R2006
    - Caution : Matlab MUST be installed in the default directory
      - For Linux : /opt or /soft
      - For Mac : /Applications
## Required package
MPTK binary files : at least version 0.5.7 (ex: “MPTK-binary-v.v.v.tar.gz”)
- Libsndfile: (tested with version 1.0.21) pre compiled library [for further informations on how to get it and where to install the file, see appendix 3.1.]
- FFTW: (tested with version 3.2.2) pre compiled library [for further informations on how to get it and where to install the file, see appendix 3.2.]
# Basic installation
## Installation procedure
Suppose you untar MPTK-binary-v.v.v.tar.gz in directory ~/foo and you want to install MPTK binary files.
The Command list you should use will look like this:

bash-3.1$ cd ~/foo
bash-3.1$ sudo ./install.sh

When using the install command to install the binary files, the shell script performs a list of command in order to copy the binary files. In this case the lines of the console log of install command should be:

–- moving files...
–- updating dynamic link libraries...
–- purging temp files...
–- MPTK has extracted itself.
## Composition of the archive
The MPTK-binary-v.v.v.tar.gz archive contains several files and directory:
- “bin” is the directory containing the MPTK executables
- “include” is the directory containing the MPTK header file « mptk.h »
- “lib” is the directory containing the useful libraries for MPTK functioning
- “mptk” is the directory containing the functionalities for MPTK
  - “matlab” is the directory containing matlab interface for MPTK
  - “plugins” is the directory containing plugins for MPTK
  - “reference” is the directory containing MPTK reference objects
  - “path.xml” is an xml file describing the path of reference and plugins tools
- “install.sh” is a shell script allowing to install MPTK files
## Installation details
When using the procedure described on paragraph 2.1. the install script copies all the files situated on the archive directory to “/usr/local/”
# Appendix
## Getting libsndfile
Libsndfile is a C library for reading and writing files containing sampled sound (such as MS Windows WAV and the Apple/SGI AIFF format) through one standard library interface. It is released in source code format under the Gnu Lesser General Public License.
This library can be downloaded either through the web (for example via Mega-Nerd website) or in the “relased files” section of the MPTK Gforge:
- http://www.mega-nerd.com/libsndfile/
- http://mptk.gforge.inria.fr/
Install this package on your computer using the instructions given on this web site will be easy an will yield the following sequence of commands after unzipping the package:
./configure [options]
make
make install
## Getting fftw
FFTW is a C subroutine library for computing the discrete Fourier transform (DFT) in one or more dimensions, of arbitrary input size, and of both real and complex data (as well as of even/odd data, i.e. the discrete cosine/sine transforms or DCT/DST).

This library can be downloaded either through the web or in the “relased files” section of the MPTK Gforge:
- http://www.fftw.org/install/windows.html
- http://mptk.gforge.inria.fr/

Install this package on your computer using the instructions given on this web site will be easy an will yield the following sequence of commands after unzipping the package:
./configure [options]
make
make install

# Help, contact and forums

If you need help with the software:
1. check if a more recent release fixes your problem;
2. if not, use the Help forum to ask questions.

Other Forums are available for open discussions about the Matching Pursuit algorithm and its MPTK implementation.
Some articles exposing scientific results related to MPTK are available in PDF format through the Released Files page.

If you want specific informations, or if you want to communicate privately with us, please write to
matching.pursuit@irisa.fr.

Request for help sent to this address won't be answered. Please use the Help forum instead.

Thank you for your interest in The Matching Pursuit ToolKit !